## Slide 1: 2025 Bayesian Modelling Workshop
Seungjae Lee
Department of Civil & Mineral Engineering
University of Toronto
May 20, 2025

## Slide 2: Instructor – Seungjae Lee

## Slide 3: Instructor – Seungjae Lee
Intelligent and Interactive Buildings Lab
Mission: Mitigate climate change and improve quality of life by realizing intelligent and interactive buildings
Create advanced AI solutions for the design and operation of building systems to improve energy performance, IEQ, occupant well-being, and grid reliability & resilience.
Explore uncharted fields of building science research to increase the depth and breadth of domain knowledge and facilitate engineering innovation.
Building System Modelling and Optimal Control
Digital Twinning
Grid-Interactive Controls
Reinforcement Learning
Uncertainty Quantification
Human-Building Interaction
Occupant Modelling
Occupant-Centric Controls
User Interface Design
Causal Inference
AI Building Expert
(Large) Language Models
Knowledge Encoding
Reinforcement Learning
Generative AI

## Slide 4: Instructor – Seungjae Lee
I am
  a building science researcher
  a big fan of Bayesian/probabilistic modelling
  interested in learning/applying/developing new methodologies
I am not (yet)
  a Bayesian statistician
  a data science methodologist

## Slide 5: Workshop Outline
This informal workshop will focus on introducing Bayesian modelling and probabilistic programming. The tentative topics covered in the 6-hour workshop include:
Measurement uncertainty and Bayesian estimation: My sensor shows 23 °C. What is the actual current temperature?
Bayesian linear regression
Informative prior probability: Do you have any prior knowledge?
Latent/unobservable variables: Bayesian way of dealing with missing information.
Advanced Topics…

## Slide 6
Measurement Uncertainty and Bayesian Estimation

## Slide 7: Measurement Uncertainty
Measuring room air temperature with a temperature sensor

## Slide 8: Measurement Uncertainty
Measuring room air temperature with a temperature sensor
Perfect sensor!

## Slide 9: Measurement Uncertainty
Accuracy (systematic error) and Precision (random error)
High Accuracy
High Precision
High Accuracy
Low Precision
Low Accuracy
High Precision
Low Accuracy
Low Precision

## Slide 10: Measurement Uncertainty
Sensor characteristic

## Slide 11: Measurement Uncertainty
Sensor characteristic

## Slide 12: Measurement Uncertainty
Sensor characteristic

## Slide 13: Measurement Uncertainty
Sensor characteristic

## Slide 14: Measurement Uncertainty
Sensor characteristic

## Slide 15: Measurement Uncertainty – Maximum Likelihood Estimation
Now, sensor reading is 23°C. What is the actual current temperature?
  Can we know?
  What is the best point estimation? 22°C? 26°C? 23°C?
This is your observation (sensor reading of 23°C)

## Slide 16: Measurement Uncertainty – Maximum Likelihood Estimation
Now, sensor reading is 23°C. What is the actual current temperature?
  Can we know?
  What is the best point estimation? 22°C? 26°C? 23°C?
If the actual temperature is 22°C, the likelihood of observing 23°C is

## Slide 17: Measurement Uncertainty – Maximum Likelihood Estimation
Now, sensor reading is 23°C. What is the actual current temperature?
  Can we know?
  What is the best point estimation? 22°C? 26°C? 23°C?
If the actual temperature is 26°C, the likelihood of observing 23°C is

## Slide 18: Measurement Uncertainty – Maximum Likelihood Estimation
Now, sensor reading is 23°C. What is the actual current temperature?
  Can we know?
  What is the best point estimation? 22°C? 26°C? 23°C?
If the actual temperature is 23°C, the likelihood of observing 23°C is
Maximum Likelihood Estimation (MLE)

## Slide 19: Measurement Uncertainty – Maximum Likelihood Estimation
You have two sensor readings, 23°C and 25°C.
What is the actual current temperature?

## Slide 20: Measurement Uncertainty – Maximum Likelihood Estimation
You have two sensor readings, 23°C and 25°C.
What is the actual current temperature?
If the actual temperature is 24°C, the likelihood of observing 23°C and 25°C is
 MLE
Things to think about: What if it’s not zero-mean Gaussian (systematic error is not zero; random error does not follow Gaussian)?

## Slide 21: Measurement Uncertainty – Bayesian Way of Thinking
Prior knowledge: Before seeing the sensor value, you thought the room temperature would be around 20°C (e.g., based on simulation results).
represents this prior knowledge, i.e., prior probability.
Prior probability distribution

## Slide 22: Measurement Uncertainty – Bayesian Way of Thinking
Prior knowledge: Before seeing the sensor value, you thought the room temperature would be around 20°C (e.g., based on simulation results).
represents this prior knowledge, i.e., prior probability.
Prior probability distribution
Prior estimation

## Slide 23: Measurement Uncertainty – Bayesian Way of Thinking
Prior knowledge: Before seeing the sensor value, you thought the room temperature would be around 20°C (e.g., based on simulation results).
represents this prior knowledge, i.e., prior probability.
Prior probability distribution
Sensor reading

## Slide 24: Measurement Uncertainty – Bayesian Way of Thinking
Sensor reading
Maximum Likelihood Estimation

## Slide 25: Measurement Uncertainty – Bayesian Way of Thinking
Sensor reading
Maximum Likelihood Estimation
Prior probability distribution

## Slide 26: Measurement Uncertainty – Bayesian Way of Thinking
Bayes’ theorem
Likelihood
Prior probability
(prior knowledge on )
Posterior probability
(updated knowledge on after observing )

## Slide 27: Measurement Uncertainty – Bayesian Way of Thinking
Sensor reading
Maximum likelihood estimation
Prior probability distribution

## Slide 28: Measurement Uncertainty – Bayesian Way of Thinking
Prior probability distribution
Sensor reading
Maximum likelihood estimation
Posterior probability distribution

## Slide 29: Measurement Uncertainty – Bayesian Way of Thinking
Prior probability distribution
Sensor reading
Posterior probability distribution
Maximum likelihood estimation
Maximum a posteriori estimation

## Slide 30: Measurement Uncertainty – Bayesian Way of Thinking
Simulation
Measurement

## Slide 31: Bayesian Update
Prior probability distribution

## Slide 32: Bayesian Update
Prior probability distribution
Posterior probability distribution
1

## Slide 33: Bayesian Update
1
2
Prior probability distribution
Posterior probability distribution

## Slide 34: Bayesian Update
1
2
Prior probability distribution
Posterior probability distribution
3

## Slide 35
Environment Setup

## Slide 36: Thank you
Seungjae Lee
sjae.lee@utoronto.ca